## Slide 1
BusBridge AXI4-Lite IP
Minor Project
Author: Jayesh
AXI4-Lite • SystemVerilog • Icarus Verilog • GTKWave

## Slide 2
Project Overview
BusBridge is an AXI4-Lite based peripheral IP block with a memory-mapped register interface.
Designed to provide control, status, data, and interrupt functionality for SoC-style integration.
The project covers RTL implementation, protocol-oriented verification, simulation, waveform inspection, and integration documentation.
BusBridge AXI4-Lite IP • Jayesh • 2

## Slide 3
Problem Statement
Develop a reusable AXI4-Lite peripheral IP block with clear register access behavior.
Support independent AXI write address and write data channels.
Provide deterministic read/write responses, including SLVERR for invalid addresses.
Add event-driven interrupt and status handling.
BusBridge AXI4-Lite IP • Jayesh • 3

## Slide 4
Objectives
Implement AXI4-Lite read and write channels in SystemVerilog.
Create configurable control/status register logic.
Support byte write strobes and memory-mapped accesses.
Verify normal transactions, error responses, interrupt behavior, and AW/W independence.
Package the design with documentation and waveform evidence.
BusBridge AXI4-Lite IP • Jayesh • 4

## Slide 5
Project Requirements & Phases
Phase 1 — Register and Protocol Planning: define register map and AXI-Lite read/write behavior.
Phase 2 — RTL Integration: create peripheral modules and interrupt/status signaling.
Phase 3 — Protocol Verification: build a compliance-oriented testbench and validate corner cases/error responses.
Phase 4 — Packaging and Reuse: provide integration documentation, constraints, and verification evidence.
BusBridge AXI4-Lite IP • Jayesh • 5

## Slide 6
System Architecture
AXI4-Lite master connects to the BusBridge AXI4-Lite slave interface.
Write address and write data are captured independently before a register write is issued.
Read addresses are accepted and corresponding register data is returned through the AXI read channel.
The register block produces ready_o and irq outputs and consumes event_i.
BusBridge AXI4-Lite IP • Jayesh • 6

## Slide 7
AXI4-Lite Interface
Write Address: AWADDR, AWVALID, AWREADY
Write Data: WDATA, WSTRB, WVALID, WREADY
Write Response: BRESP, BVALID, BREADY
Read Address: ARADDR, ARVALID, ARREADY
Read Data: RDATA, RRESP, RVALID, RREADY
Separate AW and W storage allows the channels to arrive independently.
BusBridge AXI4-Lite IP • Jayesh • 7

## Slide 8
Register Map
0x00 — CTRL: control register
0x04 — STATUS: status register
0x08 — DATA: data register
0x0C — IRQ_EN: interrupt enable
0x10 — IRQ_STATUS: interrupt status
Implemented write/read addresses return OKAY; unsupported addresses return SLVERR.
BusBridge AXI4-Lite IP • Jayesh • 8

## Slide 9
RTL Implementation
busbridge_axi_lite.sv — AXI4-Lite interface and transaction control.
busbridge_regs.sv — memory-mapped register block and peripheral behavior.
Write address/data are buffered using pending flags.
AXI responses are generated after a complete write or read transaction.
Reset is active-low through rst_n.
BusBridge AXI4-Lite IP • Jayesh • 9

## Slide 10
Verification Testbench
tb_busbridge.sv drives AXI4-Lite read/write transactions and checks responses and data.
Tests cover functional registers, interrupt behavior, error handling, and independent AW/W channels.
Simulation was performed with Icarus Verilog.
VCD output was generated for waveform inspection with GTKWave.
BusBridge AXI4-Lite IP • Jayesh • 10

## Slide 11
Simulation & Waveform
Simulation executable: sim/busbridge.vvp
Waveform database: sim/busbridge.vcd
Waveform inspected using GTKWave.
Evidence image: reports/waveform.png
Waveform evidence is included in the project repository.
BusBridge AXI4-Lite IP • Jayesh • 11

## Slide 12
Verification Results
CTRL write/read — PASS
DATA write/read — PASS
IRQ assertion after event — PASS
IRQ status set — PASS
IRQ clear — PASS
Invalid write returns SLVERR — PASS
Invalid read returns SLVERR — PASS
Independent AW/W channels — PASS
FINAL RESULT: 8 PASSED / 0 FAILED
BusBridge AXI4-Lite IP • Jayesh • 12

## Slide 13
Repository Structure
README.md — project overview and usage information
project_requirements/ — original project details and requirements
rtl/ — SystemVerilog RTL
tb/ — verification testbench
sim/ — simulation artifacts
reports/ — verification report and waveform evidence
docs/ — integration guide
constraints/ — timing/implementation constraints
scripts/ — project scripts
BusBridge AXI4-Lite IP • Jayesh • 13

## Slide 14
Conclusion
BusBridge AXI4-Lite IP was implemented and functionally verified.
All 8 planned verification checks passed with zero failures.
Simulation and GTKWave waveform evidence support the verification results.
The repository contains source, testbench, simulation evidence, requirements, and integration documentation.
Note: Vivado synthesis/implementation and lint were not performed in this project run.
BusBridge AXI4-Lite IP • Jayesh • 14

## Slide 15
GitHub / Live Project
Public GitHub repository: BusBridge-AXI4-Lite-IP
Author: Jayesh
Live repository link:
https://github.com/kolejayesh18/BusBridge-AXI4-Lite-IP
Repository contains the project source, requirements, testbench, simulation evidence, reports, waveform, and documentation.
BusBridge AXI4-Lite IP • Jayesh • 15